## Slide 1: HEALTHWARE 2.0 SMART GLUCOSE DOOR HANDLE
Tejaswi s
Sanjana r
Mentor: Dr edna elizabeth N

## Slide 2
PROBLEM STATEMENT/
WHAT’S OUR SOLUTION
METHODOLOGY
WORKING PROCESS
WHAT’S IN OUR PRESENTATION

## Slide 3: WHAT’S OUR PROBLEM STATEMENT AND SOLUTION

## Slide 4: PROBLEM STATEMENT
Diabetes is the major health concern worldwide which is due to high blood sugar levels mainly due to increase in obesity and physical inactivity
Diabetes (T1D) in young children (age 4-17 years) is rising.
It places high burden on the caretakers to monitor and control the child’s diet.
In the absence of caretakers children tend to eat sugar items which will led to complications
To avoid this we have come up with a solution - the smart glucose door handle

## Slide 5: WHAT’S OUR SOLUTION?
Our solution is basically a smart door handle.
Which can be attached to kitchen door
Locking and unlocking of the door can be controlled by the caretaker using an app

## Slide 6: METHODOLOGY

## Slide 7: METHODOLOGY
Face recognition & keypad access code(recognises caretakers/parents)- ESP32 cam module for face recognition
keypad to type in the code
CGM (continuous glucose monitor)-freestyle Libre
Scanner/receiver (freestyle Libre) attached to a handset for ease of use and Servo motor-for locking and unlocking
Arduino uno/nano(depending on size requirements) wifi rev 2- regular arduino microcontroller board with inbuilt wifi and bluetooth.
The ESP32 cam is mounted on to the arduino board and can be controlled using arduino IDE.
Freestyle libre link app

## Slide 8: METHODOLOGY
FACE RECOGNITION / PASSWORD
TEST GLUCOSE
DOOR UNLOCKS
SERVO MOTOR ANGLE(0)
SEND NOTIFICATION (LOCK/UNLOCK)
SEND GLUCOSE VALUE TO APP
SERVO MOTOR ANGLE(90)
ESP32 CAM MODULE
TRANSMITTER ON BODY(CGM)
RECEIVER ON DOOR HANDLE

## Slide 9: CGM(TRANSMITTER AND RECEIVER)

## Slide 11: CGM TECHNOLOGY
Continuous glucose monitor is one of the most recent innovations in the healthcare industry which helps diabetic patients to administer their sugar levels without pricking.
The basic cgm device contains a sensor plus transmitter which is implanted into the body of the patient .
The transmitter sends the values collected by the sensor to either a receiver or other devices via bLE(bluetooth low energy).
There are several brands providing this product along with an inbuilt app to survey and analyse the sugar levels.
Some of these apps are also linked to other apps providing diet tips and routines.

## Slide 12
Dexcom G6
Abbott Freestyle Libre
The cgm may send notifications to a receiver or sometimes directly to mobiles to prevent the disturbance of carrying around a receiver.
The freestyle Libre provides cgm sensors which updates values only when the receiver or mobile is scanned against the sensor/transmitter unlike other companies such as dexcom which automatically updates the sugar levels to the nearby connected device
BACK

## Slide 13: UPLOAD GLUCOSE VALUES TO CLOUD
The earlier methods of uploading data to cloud was by connecting the receiver of the CGM to a computer via USB.
This is not a very efficient way to store data and give access to medical practitioners
A recent patent has been applied in the US for the direct CGMconnectivity to the storage device of the cloud.
According to this , an internet gateway chip is attached to the receiver which sends data to the cloud wirelessly

## Slide 14: APP FEATURES
Since we send all the glucose values to cloud we can notify those values through an app to the parent
And allow the parent to open or lock the handle
And using these glucose values we can create an alert alarm if the values are too high or low
In the same app we can plot graphs for various timeline which can be used for medical examination

## Slide 15: CLOUD DATA MANAGEMENT
Since we are dealing with important medical records proper cloud data management is of utmost importance.
Cloud data management is very different from traditional data management methods and has several advantages such as
security,
zero maintenance,
automated backup and so on.
There are several companies which offer to provide data management services at low costs.

## Slide 16: ESP32 CAM
Faces of caretakers can be enrolled in esp32cam server
If enrolled face comes near the door can be unlocked
BACK

## Slide 17: KEYPAD AND SERVO MOTOR

## Slide 18: WORKING PROCESS

## Slide 19: WORKING PROCESS
Case 1 :
A non diabetic person needs to access the door, can unlock by using facial recognition/passcode
Case 2:
  A diabetic person needs to use the device, they need to use the scanner to test the glucose level in their body and the receiver will send notification to an app in their device.
  The parent can choose to unlock or not .
  And these scanned glucose values will be stored in cloud and sent to an app which can be used to analyse the health conditions of the child and take necessary precautions if necessary.

## Slide 20: INSTALLATION PROCESS
Lorem ipsum dolor sit amet, consectetur adipiscing. Lorem ipsum dolor sit.
Lorem ipsum dolor sit amet, consectetur adipiscing. Lorem ipsum dolor sit.
Lorem ipsum dolor sit amet, consectetur adipiscing. Lorem ipsum dolr sit.
Lorem ipsum dolor sit amet, consectetur adipiscing. Lorem ipsum dolor sit.
ATTACH THE HANDLE TO DOOR
SET UP THE APP
ENROL FACES OF CARETAKERS AND NONDIABETIC FAMILY MEMBERS
ATTACH TRANSMITTER TO BODY

## Slide 21: NOVELTY
Integrating recent CGM technology with a smart door lock system
Combines diet control as well as glucose measuring feature
Alarm systems
Access your glucose value history anywhere
Since values are stored in cloud there are no chances of losing the glucose history data
Plot graphs and analysis which can be used for medical examination
Parent can see the child’s glucose value from anywhere automatically
Mobile door handle can be used anywhere

## Slide 22: IS CGM SAFE? WHY USE CGM?
The Freestyle Libre is available for age 4 and older
It is safe and more comfortable than pricking child finger 7 times a day
Mainly used during the initial stage of diabetes to get an idea about the child’s glucose trend
And also useful for patients with comorbidities to regularly have an eye on their glucose reading rather than pricking
Recommended by doctors
It is accurate

## Slide 23: WHY USE CGM?
It is water resistant but not waterproof thus allowing basic level water involved activities.
However we can make it more water resistant by sticking an adhesive water resistant patch over it which is easily available in the market.
It can be made more attractive to the younger age groups by including various colors and patterns that make it consumer attractive.
For example we can have superman or other superhero pictures on it to make it look fashionable so that kids don’t remove it

## Slide 24: CONCLUSION
The most commonly used term now in the field of diabetology is the continuous glucose monitor which has simplified the lives of many . We want to take it a step further and introduce the automated door handle targeting the diabetic audience especially children of age group 7-12.
In the absence of caretakers , when the child accesses the kitchen door and scans the cgm sensor/transmitter with the door handle containing the receiver , the blood sugar levels are displayed on the monitor and also sent as a notification to the supervisors device. By taking a look at the values, the adult can choose to open the kitchen door with just a click in their apps.
For the non diabetic members of the family , we use face recognition and for the visitors , the access code.
The main objective of this initiative is to widen and integrate the recent technology and advancements to provide unique yet feasible solutions to day to day problems.

## Slide 25: REFERENCES
FreeStyle Libre Sensor - Flash Glucose - Abbott Libre India
https://www.tinkercad.com/
https://www.arduino.cc/

## Slide 26: THANK YOU!